April 6, 2021

Dear Westport Water Customer,

The Town of Westport is a registered Public Water Supply with the Massachusetts Department of Environmental Protection, Drinking Water Program.  The Public Water Supply Identification Number (PWSID #) is 4334090. The Town’s water distribution system begins at the Fall River/Westport boundary and travels in an Easterly direction along Route 6 to the Davis Road area.

If you receive your drinking water from the Town’s distribution system then you are receiving 100% of your water from the Fall River Water Department.  Enclosed is a Fall River Water Department Consumer Confidence Report, which provides information concerning the water supply, distribution and water quality.

The Town of Westport is required to sample it's distribution system for Trihalomethanes and Haloacetic Acids which are byproducts that are produced when organic matter combines with chlorine.  The Town is also required to sample for Lead and Copper at the customers home.  Below are the sample results.

Name 	MCL	MCLG	Detection	      Westport	Sample Date 	Violation	     Major Source in Drinking Water		Limit	       Results

Inorganic Contaminants, measured in parts per million

Free Chlorine 	4.0	4.0		      0.33 - .84	7/14/20 & 11/17/20	      No 	     Added during treatment

process to kill bacteria

Lead, ppb	15	0	     1	     ND – 5		9/17/19		      No	     Corrosion of household

plumbing

Copper, ppm	1.3	0	 0.003	     ND – 0.004	9/17/19	      No		     Corrosion of household

plumbing

Volatile Organic Contaminants, measured in parts per billion, (ppb)

Trihalomethanes 	80 ug/L	n/a	   0.5	     41 – 86	 	8/15/20		      Yes	     Reaction by-product of

chlorine and

residual organic materials

Haloacetic acids	60 ug/L	n/a	   1.0	     18 – 27		8/15/20		      Yes	     Reaction by-product of

chlorine and residual

organic materials

The Town of Westport has worked diligently to flush the distribution system and installed blow off valves to reduce the water residence time, the sampling frequency has been reduced to quarterly sampling.

A violation for Disinfection By Products, Total Trihalomethanes and Haloacetic Acids 5 occurred during the monitoring period of November 1n 2020 – November 30.  The public water supply failed to sample and report the results within the required timeframe.  A proposed Action Plan is to assign the contracted Massachusetts Certified Water Operator or designee to collect all scheduled water quality samples for analysis and report the results to the Department of Environmental Protection, Drinking Water Program within the required time frame.

This is not an immediate risk.  However, some people who drink water containing Trihalomethanes in excess of the MCL over many years may experience problems with their liver, kidneys or central nervous system and may have an increased risk of getting cancer.

If you have any questions concerning this Consumer Confidence Report, please contact Denise Bouchard at (508) 636-1004 at the Selectmen’s office or Linda L. Correia, Massachusetts Certified Water Operator at (508) 674-2832.

Thank you,

BOARD OF SELECTMEN

TOWN OF WESTPORT

# Text boxes

TOWN OF WESTPORT

MASSACHUSETTS 02790

###### BOARD OF SELECTMEN

WATER DEPARTMENT

Tel. (508) 636-1004

Fax. (508) 636-1147